## Slide 1: UNIT-2 CHEMICAL PROPELLANTS
By
A.VinothKumar
Assistant Professor
Department of Aerospace Engineering
SRM University

## Slide 2: UNIT-2 SYLLABUS
Molecular mass.
Specific heat ratio.
Energy release during combustion.
Stoichiometry & mixture ratio.
Criterion for choice of propellant.
Solid propellants - requirement, composition and processing.
Liquid propellants- energy content, storability.
Types and classifications.
Numerical problems

## Slide 3: Molecular mass
Molecular mass or molecular weight is the mass of a molecule.
It is calculated as the sum of the mass of each constituent atom multiplied by the number of atoms of that element in the molecular formula.
Elements having lower atomic mass are preferred to obtain lower molecular mass of the combustion gases.
Chart: Atomic Number of Light Elements
| H | Li | Be | Bo | C | N | O | F | Al | S | Cl
Series 1 | 1 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 13 | 16 | 17

## Slide 4: Specific heat
The specific heat is the amount of heat per unit mass required to raise the temperature by one degree Celsius.
The specific heat of a gas increases as its molecular structure become more complex. So the gases having lower specific heat are preferred.
Chart: 
| He | He | O | H2 | OH | Hcl | N2 | CO | NO | O2 | H2O | CO2
2000K | 20.8 | 20.8 | 20.8 | 34.3 | 34.7 | 35.6 | 36 | 36.4 | 36.8 | 37.7 | 51 | 60.2
3000K | 20.8 | 20.8 | 20.8 | 20.9 | 38.9 | 38.1 | 38.1 | 37.7 | 38.1 | 41.4 | 58.2 | 63.6

## Slide 5: Specific heat ratio
It is defined as the ratio of the Specific heat at constant pressure to the Specific heat at constant volume.
Smaller values of specific heat is preferred to obtain higher values of characteristic velocity

## Slide 6: Energy release during combustion
Case 1
Case 2
The heat released by case 1 is higher than that of case2 because of formation of carbon monoxide in case2

## Slide 7: Stoichiometry & mixture ratio
Stoichiometry
    The term Stoichiometry refers to the amount of fuel and oxidizer which leads to fuel being completely oxidised by forming the completely oxidised product, which in turn releases maximum amount of energy.
Mixture Ratio(MR)
  It is defined as the ratio of mass of the oxidiser to the mass of fuel taking part in combustion.
  The mixture ratio corresponds to stoichiometric composition is called as stoichiometric mixture ratio(MR)stoi.
Fuel richMR<(MR)stoi

## Slide 8: Equivalence ratio
It is defined as the ratio of actual fuel to air mass ratio to that of stoichiometric fuel to air mass ratio.